## Slide 1: SoI — Proof of Concept (PoC) Stage Template
Team: The Spark
Lead: Sibithra V
Members: Sakthivel V, Shri krishnamoorthi S, Viviksha K,
Arun R
Mentor: Sriram | SoI Lab Code: EI| Cohort: 2024-28

## Slide 2: Problem Statement
The increasing presence of microplastics in water sources and drinking supplies poses serious risks to health and the environment. Despite advances in water treatment, no cost-effective and efficient system currently exists to detect and quantify microplastics in real time. This lack of monitoring threatens water safety and weakens public trust.

## Slide 3: End‑User Recap
Target End-User: • Who — Water treatment plants, municipal water boards, environmental monitoring agencies, research labs • Where — Real-time monitoring points in treatment facilities, reservoirs, rivers, industrial discharge outlets • When — During continuous water purification and regulatory compliance checks

## Slide 4: EVIDENCES
Evidence: • Studies show microplastics detected in >90% of sampled bottled and tap water worldwide • Current detection methods take hours–days in laboratory settings and require costly instruments, preventing real-time corrective action
https://www.nih.gov/news-events/nih-research-matters/plastic-particles-bottled-water?utm_source
https://www.mdpi.com/2673-8929/4/2/24?utm_source
https://www.dw.com/en/bottled-water-not-safe-from-microplastic-contamination/a-42936246?utm_source
https://www.sciencedirect.com/science/article/pii/S0043135419301794
https://pubmed.ncbi.nlm.nih.gov/38537794/

## Slide 5: Success Metrics for the End-User
• Time saved: Real-time or near-instant detection vs. hours/days of lab analysis • Error reduced: Higher accuracy and repeatability compared to manual sampling and lab processing • Cost lowered: Reduced labor, testing, and compliance costs via automated on-site monitoring • Risk lowered: Earlier contamination detection , improved safety and reduced regulatory penalties

## Slide 6: Selected Idea Recap & Value Proposition
Concept Summary:
Microplastics are widespread in rivers, oceans, and drinking water, with studies showing up to 80% of global tap water contaminated. Current detection methods are accurate but slow, costly, and lab-dependent. A proposed solution is a portable, low-cost system using sensor technologies, microfluidics, and AI to enable quick and reliable microplastic detection.
Key Features:
-Low Cost – Affordable sensors for large-scale monitoring
-Portable – On-site testing anytime, anywhere
-Fast Results – Quick detection within hours
Value Proposition:
Low cost parts are enough for more accuracy and it can able to give fast results within <=2 seconds. System can be stable <=24 hours.

## Slide 7: PoC Objectives & Success Criteria
Critical Assumption / Question | Metric | Target Threshold | Test Method
Sensor can detect microplastics | Signal change | Visible difference | Clean vs spiked water
Low-cost parts are enough | Accuracy | ≥ 80% | Compare with reference
Detection must be fast | Time | ≤ 2 s | Run flowing water and check display response time
System must be stable | Drift | Low over 24 h | Keep device ON for 24 hours and record readings
Output must be clear | User understanding | Few errors | Show to 5–10 users and check if they interpret correctly
Notes: Define 3–5 success criteria before building. Use measurable targets (e.g., accuracy ≥90%, latency ≤1s).

## Slide 8: Scope, Assumptions & Constraints
In Scope: Real-time microplastic detection using low-cost sensor + OLED display Out of Scope: Classification, large-scale deployment, cloud or filtration integration Assumptions: Test water available, indoor use, basic user skill Constraints: Limited budget/time, no advanced lab, safety required

## Slide 9: System Overview — Architecture / Design
Water sample collection
Laser light
Photodiode sensor
LM358 Amplifier
Arduino UNO
LCD Display
Contamination status

## Slide 10: Build Plan & Timeline
Phase / Week | Tasks / Milestones | Owner(s) | Status / Date
Week 1 | Literature review & block-diagram finalization | Team | Done
Week 2 | Components sourcing & bench wiring (laser + PD + LM358) | Team | Done
Week 3 | ESP32 ADC read + threshold logic + OLED display | Team | Done
Week 4 | PoC integration test with clean vs contaminated water | Team | Done
Week 5 | Documentation + PPT + demo video recording | Team | Done
Notes: Plan short, focused sprints. Keep the PoC within a few weeks. Update status as you progress.

## Slide 11: Resources & Budget
Item / Tool | Qty / Spec | Cost (₹) | Source / Link | Notes
Laser Diode | 1 | ~100 | Amazon / Local store | Light scattering source
Photodiode sensor | 1 | ~150 | Amazon | Detects scattered light
LM358 - Amplifier | 1 | ~50 | Local store | For amplifiying
Arduino UNO | 1 | ~650 | Amazon | ADC + logic + display drive
OLED Display (0.96") | 1 | ~200 | Amazon | Real-time display
Breadboard + Wires | 1 set | ~150 | Local store | For prototyping
Microplastics sample | - | ~0 -100 | Salt water + crushed plastic | Mock test sample
Notes: List only what is necessary to prove the concept (hardware, datasets, APIs, cloud credits, software, etc.).

## Slide 12: Demo & Test Plan
Demo Scenario • Show live setup (laser + photodiode + LM358 + ESP32 + OLED) • Test with clean water vs microplastic-mixed water • OLED changes to “Detected” when contaminated sample inserted
Audience • Mentors
Test Protocols • Two samples: clean RO water & plastic-spiked water • ≥ 3–5 repeat runs for each sample • Check stable difference in sensor output & correct alert • Indoor bench test to avoid light interference
Pre-Demo Checklist • Align laser & photodiode, reset ESP32 reading • Prepare labeled test cups (clean / contaminated) • Safety: no water near electronics, tissue/cloth nearby

## Slide 13: Evidence — Results & Findings
Metric (from criteria) | Target | Observed | Pass/Gap | Notes / Evidence Link
Sensor response to microplastics | Clear change from clean baseline | 12–18% signal shift detected | Pass | Response repeats when sample reintroduced
Detection time | ≤ 2 seconds | ~1.3 seconds | Pass | Measured with stopwatch
Repeatability | Consistent over ≥5 trials | 4/5 consistent | Gap | One trial noisy
Hardware budget | ~3500 | 3450 | Pass | Within limit
Safety & handling | No spill risk near electronics | Enclosure prevents contact | Minor gap | Acrylic housing tested
User readability | OLED clean vs detected clearly shown | Contrast visible but could be brighter | Pass | Clarity issue
Notes: Attach graphs/screens, include data tables where possible. Link raw logs/notebooks where relevant.

## Slide 14: Demo Video & Repositories
Repository Link:
https://github.com/Sibithra/Detection-of-Microplastics-in-Water-
Demo Video:
https://uploadnow.io/f/PpMFvx7

## Slide 15: Risks, Limitations & Mitigations
Risk / Limitation | Impact (H/M/L) | Likelihood (H/M/L) | Mitigation / Plan | Owner
Ambient light interference | Medium | Medium | Shield sensor / test indoors | Team
Water spill on electronics | High | Medium | Use cups, drip tray, tissue, spacing | Team
Laser–PD misalignment | High | Medium | Fix mounts, mark alignment points | Team
Microplastic test sample availability | Medium | Low | Prepare small DIY spiked samples | Team
Budget overrun | Low | Low | Use only essential components | Team
Notes: Include technical, safety, privacy, compliance, and supply risks. Address early showstoppers.

## Slide 16: Go/No‑Go & Next Steps → Prototype
Decision Refine & Re-test — Signals and logic are promising, but repeatability & stability need confirmation before advancing.
Prototype Plan (after refine) • Stabilize optics + reduce ambient noise • Add auto-baseline / simple calibration • Add enclosure & safe sample holder Timeline: 1–2 weeks refinement + re-test Needs: Mounts, sample sets, test time
KPIs to Carry Forward • ≥5/5 consistent detections • ≤2 s response time • <5% drift in 24 h • Within PoC budget • Clear unambiguous alert on display