## Slide 1
SoI — Prototype Stage
Submission Deck Template
Team Details (fill)
Team: The Spark | Team-ID: P-2024-28-EI-159
Lead: Sibithra V | Members: Sakthivel V, Viviksha K,
Arun R, Shri krishnamoorthy S
Mentor: Sriram | Lab Code: EI
Cohort: 2024 - 2028 | Date: 2026-01-27

## Slide 2
SoI Innovation Pipeline
CONTEXT
Problem & End-User Recap
Problem statement (≤150 words)
Microplastics are widely present in drinking water, but current detection methods are slow, expensive, and lab-dependent. This prevents real-time monitoring and timely action to ensure water safety.
Target end-user / context
Water treatment plants, municipal boards, environmental agencies.
Evidence
80% water samples contain microplastics; lab tests take hours–days.
https://pubmed.ncbi.nlm.nih.gov/38537794/
Success metric(s)
Fast detection, lower testing cost, early contamination alerts.
SoI Prototype Stage — Submission Deck
3/23

## Slide 3
SoI Innovation Pipeline
IDEATION
Ideation Recap — Options Explored & Selected Idea
Ideas explored (≥3)
Ideas: Laser + photodiode detection, IR turbidity sensing, Camera + filtration
Selected idea (taken to PoC)
A portable, low-cost optical detection system using a laser, photodiode, and microcontroller for real-time alerts.
Why selected
Chosen for its quick on-site detection (desirable), use of affordable components (feasible), and scalability for large-scale monitoring (viable).
MoSCoW: Must-have features for PoC
Optical sensing, signal amplification and processing, and instant contamination display.
SoI Prototype Stage — Submission Deck
4/23

## Slide 4
SoI Innovation Pipeline
POC
PoC Recap — What We Built & Learned
Summarize PoC outcomes and gaps that drive prototype.
PoC summary
PoC built
An optical microplastic detection setup using a laser, photodiode, signal amplifier, microcontroller, and LCD display.
PoC focus
To prove the feasibility of real-time microplastic detection using low-cost optical sensing.
PoC evidence
The system showed a clear difference between clean and contaminated water with response time under 2 seconds.
Key gaps
Signal noise, alignment sensitivity, and repeatability need improvement before prototype scaling.
SoI Prototype Stage — Submission Deck
5/23

## Slide 5
SoI Innovation Pipeline
PLAN
Prototype Objectives & Success Criteria
Define what “success” means and how you will test.
Prototype objective / risk to reduce
Metric
Target
How we will test
Reliable detection
Accuracy
≥ 90%
Test with clean vs plastic-mixed water
Fast response
Detection time
≤ 2 seconds
Measure time from sample insert to LCD update
Signal stability
Drift
< 5% in 24 hrs
Continuous reading with same sample
Low false alerts
False positives
≤ 1 in 10
Test under room light conditions
Add 3–5 rows. Keep it measurable.
SoI Prototype Stage — Submission Deck
6/23

## Slide 6
SoI Innovation Pipeline
STRATEGY
Prototype Strategy
Works-like functional
Why this option: Main risk is whether the hardware can reliably detect microplastics and give fast alerts. End-to-end sensor → amplifier → Arduino → LCD must work with measurable performance.
Your plan (short):
v1 goal: Stable detection with fixed laser–sensor alignment
Integrations: Laser → BPW34 → LM358 → Arduino → LCD
Done when: ≥90% correct detection, ≤2 s response
Validation: Repeated tests with clean vs plastic water
SoI Prototype Stage — Submission Deck
7/23

## Slide 7
SoI Innovation Pipeline
STRATEGY
Prototype Strategy Option A
Works-like functional (integration & metrics first)
OPTION A
My plan:
Why this fits
Main risk is hardware integration and reliable optical detection.
v1 goal
Stable detection of microplastics with fixed laser–sensor setup.
Integrations
Laser → BPW34 photodiode → LM358 → Arduino UNO → LCD display.
Definition of Done
LCD shows correct result in ≥90% of tests with ≤2 s response.
Validation + metrics
Accuracy, response time, signal stability (drift <5% in 24 hrs).
SoI Prototype Stage — Submission Deck
8/23

## Slide 8
SoI Innovation Pipeline
SCOPE
Prototype Scope, Requirements & Constraints
Define what you WILL build, and what you WON’T (for now).
Scope
In scope
Optical sensing, signal amplification, microcontroller processing, and LCD-based contamination alerts.
Out of scope
Microplastic classification, cloud connectivity, large-scale deployment, field trials.
Assumptions
Indoor testing environment, controlled lighting, and availability of test water samples.
Constraints
Limited time, budget, and safety considerations for electronic components.
Acceptance checks (3–5)
SoI Prototype Stage — Submission Deck
12/23
LCD update ≤ 2 seconds after sample is placed.
Detection accuracy ≥ 90% over 20 test runs.
Signal drift < 5% in 24 hours with same sample.
False alerts ≤ 1 in 10 tests under room light.
System runs continuously for 1 hour without reset.

## Slide 9
SoI Innovation Pipeline
DESIGN
Prototype System Overview — Architecture / Design
.
13/23
Water sample collection
Laser light
Photodiode sensor
LM358 Amplifier
Arduino UNO
LCD Display
Contamination status
Data Flow: Analog light signal → amplified voltage → digital decision → visual alert Interfaces: Analog signal to Arduino ADC, I2C to LCD Tech Stack: Embedded C (Arduino IDE), discrete analog electronics Simulated Parts: None (all components are real)

## Slide 10
SoI Innovation Pipeline
BUILD
Prototype Build Plan & Timeline (Sprints)
Break work into 2–4 short sprints. Each ends with a demoable increment.
Sprint / Week
Key tasks & deliverables
Owner(s)
Status
Sprint 1
Laser–photodiode alignment and ambient light reduction
Team
Planned
Sprint 2
Amplifier tuning and arduino firmware stabilization
Team
Planned
Sprint 3
Enclosure setup and safety checks
Team
Planned
Sprint 4
Repeated testing and result validation
Team
Planned
SoI Prototype Stage — Submission Deck
14/23

## Slide 11
SoI Innovation Pipeline
RESOURCES
Resources, BOM & Budget
Item / resource
Qty
Unit cost
Source
Notes
Laser diode
1
20
Local electronics shop
Light source
Photodiode sensor(BPW34)
1
80
Local electronics shop
Optical sensor
LM 358 OP-Amp
1
7
Local electronics shop
Signal amplifier
Arduino UNO
1
450
Local electronics shop
Main controller
Arduino UNO Cable
1
35
Local electronics shop
Programming & power
Bread board
1
54
Local electronics shop
Circuit setup
Jumper Wires
As required
45
Local electronics shop
Connections
16*2 LCD Display
1
174
Local electronics shop
Output display
Transparent beaker
1
15
Local electronics shop
Water sample

## Slide 12
SoI Innovation Pipeline
VALIDATE
Prototype Demo & Validation Plan
What you will show, how you will test, and what evidence you will capture.
Demo scenario
Describe the end-to-end demo in 4–6 steps.
1.Power ON Arduino and LCD.
2.Place beaker with clean water → LCD shows “No Contamination”.
3.Add crushed plastic to water.
4.Laser light scatters; sensor value changes.
5.LCD updates to “Detected”.
6.Repeat test for confirmation.
Audience: Mentors / Judges Duration: ≤ 2 min video
Validation protocols (fill)
*Test cases / sample size: Clean water vs plastic-mixed water, 20 total runs
*Environment: Indoor bench setup, controlled lighting
*What we measure: Detection accuracy, response time, signal stability
*Pass/Fail: Accuracy ≥90%, response ≤2 s, false alerts ≤1 in 10
Usability check: Team members perform sample swap and observe clarity of LCD message.
SoI Prototype Stage — Submission Deck
16/23

## Slide 13
SoI Innovation Pipeline
EVIDENCE
Evidence — Prototype Results & Iterations
Show what improved from v1 → v2, with evidence.
Version
What changed
Test run
Result
Evidence link
v0
Basic laser–BPW34 setup on breadboard
10 runs
Detection inconsistent, noise present
v1
Fixed laser–sensor alignment, stable wiring
15 runs
Clear signal difference, ~85% accuracy
v2
Added threshold tuning and signal averaging
20 runs
≥90% accuracy, faster LCD update
v3
Reduced ambient light using cover
20 runs
False alerts reduced significantly
SoI Prototype Stage — Submission Deck
17/23

## Slide 14
SoI Innovation Pipeline
LINKS
Prototype Demo & Artifacts
Links
Demo video file upload (MP4, ≤2 min)
https://www.kapwing.com/videos/69772fca3696ef8bc5738c06
Repository URL
https://github.com/Sibithra/Detection-of-Microplastics-in-Water-/tree/main/Detection-of-Microplastics-in-Water-
Build files (CAD/PCB)
Not applicable — breadboard-based prototype
Dataset / logs
Arduino serial monitor logs and test readings (clean vs plastic water)
Release / version
v1.0-prototype
SoI Prototype Stage — Submission Deck
18/23

## Slide 15
SoI Innovation Pipeline
RISK
Risks, Limitations & Mitigations
Be honest. Show how you will reduce risk before MVP.
Risk / limitation
Impact (L/M/H)
Likelihood
Mitigation / next action
Ambient light interference
High
Medium
Enclosure and optical shielding
Signal drift over time
Medium
Medium
Auto-baseline and periodic calibration
Laser–sensor misalignment
Medium
Low
Fixed mounts and alignment checks
Limited detection accuracy
Medium
Medium
Multiple test runs and threshold tuning
Water–electronics safety risk
High
Low
Insulated wiring and sealed sample holder
SoI Prototype Stage — Submission Deck
19/23

## Slide 16
SoI Innovation Pipeline
DECISION
Go / Refine / Pivot & Next Steps → MVP
Decision (fill)
Decision: REFINE & RE-TEST
Rationale (tie to metrics):
Next steps toward MVP (not MVP itself)
* Build enclosed optical chamber to block external light.
* Add auto-calibration and baseline correction in Arduino code.
* Perform long-duration stability testing (24–48 hrs).
KPIs to Carry Forward
* Detection accuracy ≥95%
* Response time ≤2 seconds
* Signal drift <5% per day
* False alerts ≤5%
]
SoI Prototype Stage — Submission Deck
20/23
Accuracy reached ~90% but needs improvement to ≥95%.
Signal drift observed over long runs.
Ambient light still affects readings.

## Slide 17
SoI Innovation Pipeline
REFS
References
[1] NIH Research Matters, “Plastic particles in bottled water,” National Institutes of Health, 2024. URL: https://www.nih.gov/news-events/nih-research-matters/plastic-particles-bottled-water (accessed 2026-01-20).
[2] A. Shrivastava et al., “Microplastics in drinking water: Detection and challenges,” MDPI Sensors, vol. 4, no. 2, 2024. URL: https://www.mdpi.com/2673-8929/4/2/24 (accessed 2026-01-20).
[3] Deutsche Welle, “Bottled water not safe from microplastic contamination,” 2018. URL: https://www.dw.com/en/bottled-water-not-safe-from-microplastic-contamination/a-42936246 (accessed 2026-01-20).
[4] S. Mintenig et al., “Low numbers of microplastics detected in drinking water,” Water Research, vol. 142, pp. 488–495, 2019. URL: https://www.sciencedirect.com/science/article/pii/S0043135419301794 (accessed 2026-01-20).
[5] PubMed, “Microplastic exposure via drinking water,” PubMed ID: 38537794, 2024. URL: https://pubmed.ncbi.nlm.nih.gov/38537794/ (accessed 2026-01-20).
SoI Prototype Stage — Submission Deck
21/23